## Slide 1
Red Planet Recycle
An Investigation Into Advanced Life Support system for Mars
Tuesday 24th January, 2 PM
Chemical Engineering
Design Projects 4

## Slide 2
Outline
Design objectives
Stages 1 & 2 outline
Criteria & Constraints
Water treatment
Air treatment
Discussion

## Slide 3
Outline
1. Design
objectives
Design Brief
Your consulting company has been hired by the Mars Exploration Consortium, represented by Drs. Sarkisov and Valluri. The objective of the consortium is to build a space station on Mars, capable of a continuous support of a 10 member crew. It has been planned that a re-supply mission should return to Mars every 18 months, with the main resources re-supplied being water, oxygen and food. With the current cost of the re-supplement estimated at £1 M/kg, there is a clear need for intensive onsite recycling of the resources, including water, air and waste. Your company has been hired to develop an integrated recycling solution, with an objective to minimize the weight of the re-supplement cargo. Other technologies that should be explored along with the recycling, include collection and purification of water on Mars and local production of food stock (high protein vegetables etc). The primary source of energy for the Martial station will be provided by a nuclear reactor with up to 50 MWe capacity.

## Slide 4
Outline
1. Design
objectives
Design Outline
We have identified 3 key stages of the design:
Resource requirements assuming no recycling or utilisation of local sources
Resource requirements with recycling introduced
Resource requirements with recycling introduced and utilisation of local resources. Investigation into unconventional technologies

## Slide 5
Outline
1. Design
objectives
Using previous isolated systems as examples the essential resources that must be controlled in a life support system are:
Water
Air
Food
Waste
Thermal energy
Biomass
The last three require control but no resupply on the Mars space station, therefore these are not considered at this stage of design.
2. Stages
1&2 Outline
Stage 1 – Design basis

## Slide 6
Outline
1. Design
objectives
Stage 1 – Resource requirements
Total Water Requirement |  |  | 
Drinking | Hygiene* | Safety | Total
[kg] | [kg] | [kg] | [kg]
17472 | 92345 | 27454.25 | 137271.25
Total Air Requirement |  |  |  | 
N2 | O2 | CO2 | Safety | Total
[kg] | [kg] | [kg] | [kg] | [kg]
0 | 4599 | 0 | 1149.75 | 5748.75
Calorific requirement |  | 
Standard | Safety | Total
[MJ] | [MJ] | [MJ]
57.3 | 14.325 | 71.625
Total Oxygen | Total Water | Total Resupply Weight | Total Resupply Cost
[kg] | [kg] | [kg] | [£Million]
5748.75 | 137271.25 | 143020 | 143020
2. Stages
1&2 Outline

## Slide 7
Outline
1. Design
objectives
Design Outlook
Stage 1 | Stage 2 | Stage 3
2. Stages
1&2 Outline

## Slide 8
Outline
1. Design
objectives
Stage 2 – Design basis
Stage2: Introducing recycling processes to the Mars space station in order to minimise the resupply requirements
Of the three focus resources identified in stage one, only two can effectively be recycled. These are:
Water
Air
2. Stages
1&2 Outline

## Slide 9
Outline
1. Design
objectives
Water Recycling
Assumptions:
All consumed water requires recycling
Assuming NASA standard water composition
2. Stages
1&2 Outline

## Slide 10
Outline
1. Design
objectives
Water Recycling Design Basis
Stage 1
Water
Waste water
(ppm)
Treated water
(ppm)
Ammonia 55 calcium 0.9
chlorine 229 phosphate 134 sulphate 80 Nitrate <100 sodium 150 potassium 133 magnesium 1.5 TOC >11
Ammonia 0.05 calcium 30
chlorine 200 phosphate N/A sulphate 250 Nitrate 10 sodium N/A potassium 340 magnesium 50 TOC <0.5
Flowrate 200.6 kg/day
2. Stages
1&2 Outline
M.Flynn (1998)

## Slide 11: ?
Outline
1. Design
objectives
Air Recycling
Assumptions:
The air treatment is split into three distinct processes: CO2 separation, CO2 consumption and O2 production
Assuming same composition of air as on Earth
Assume N2 is a buffer
2. Stages
1&2 Outline

## Slide 12: ?
Outline
1. Design
objectives
Air Recycling Design Basis
Stage 1
Air
Pre-treatment
10 kg/day CO2
Stage 1
Air
Air treatment
8.4 kg/day O2
Air
Air
2. Stages
1&2 Outline

## Slide 13
Outline
1. Design
objectives
Criteria & Constraints
Applicability
Reliability
Modularity
Resupply
But in general we look for the technology to be;
Lightweight and economical, able to recover a high percentage of waste water and operate with minimal consumables
2. Stages
1&2 Outline
3. Criteria &
Constraints

## Slide 14: ?
Outline
1. Design
objectives
Criteria & Constraints- Water treatment
2. Criteria & constraints
Technology | Applicability | Reliability | Modularity | Resupply
VPCAR |  |  |  | 
DOC |  |  |  | 
Electrocoagulation |  |  |  | ?
Microorganism based |  | - | - | -
ISS |  |  |  | 
Membrane |  |  |  | 
Advanced oxidation |  | - | - | -
Ecocyclet |  | - | - | -
UV treatment |  | - | - | -
4. Water
treatment
2. Stages
1&2 Outline
3. Criteria &
Constraints

## Slide 15: ?
Outline
1. Design
objectives
Criteria & Constraints- Water treatments
Technology | Applicability | Reliability | Modularity | Resupply
VPCAR |  |  |  | 
DOC |  |  |  | 
Electrocoagulation |  |  |  | ?
Microorganism based |  | - | - | -
ISS |  |  |  | 
Membrane |  |  |  | 
Advanced oxidation |  | - | - | -
Ecocyclet |  | - | - | -
UV treatment |  | - | - | -
4. Water
treatment
2. Stages
1&2 Outline
3. Criteria &
Constraints

## Slide 16: ?
Outline
1. Design
objectives
Water treatment- Final 5
2. Criteria & constraints
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 92 | - | 99 | 90
Maintanence | Unknown | - | 50 days | >18 months
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 92 | - | 99 | 
Maintanence | Unknown | - | 50 days | >18 months
4. Water
treatment
3. Stages
1&2 Outline

## Slide 17: ?
Outline
1. Design
objectives
Water treatment- Final 5
2. Criteria & constraints
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 92 | - | 99 | 90
Maintanence | Unknown | - | 50 days | >18 months
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 92 | - | 99 | 
Maintanence | Unknown | - | 50 days | >18 months
4. Water
treatment
3. Stages
1&2 Outline

## Slide 18: ?
CO2 Separation
CDRA - Carbon Dioxide Removal Assembly (ISS)
PSA – Pressure Swing Adsorption
MEA CO2 Absorption
Activated Carbon Absorption
Scrubbers
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 19: ?
1. CDRA – Process Description
Utilises regenerative molecular sieve technology to remove carbon dioxide.
In the CDRA, there are four beds of two different zeolites.
Zeolite 13x absorbs water, while zeolite 5A absorbs carbon dioxide.
Each side of the CDRA contains a zeolite 13X connected to a zeolite 5A bed.
As the air passes through the zeolite 13X bed, water gets trapped and removed from the air.
The dried air goes into the zeolite 5A bed where carbon dioxide gets trapped and removed.
The outgoing air is then dry and free from carbon dioxide.
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 20: ?
1. CDRA – Simplified PFD
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 21: ?
2. PSA – Process Description
Similar process to the CDRA with the exception that pressure is used instead of heat.
Beds are operated at 150kPa or higher.
Higher the pressure, the more CO2 is adsorbed.
When bed becomes saturated it is depressurised to atmospheric levels.
CO2 is released from the bed and the regeneration is complete.
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 22: ?
3. MEA CO2 Absorption
This is a regenerative method of removing CO2 from air.
Uses an aqueous solution of 25-30 wt.% (4-5 M) monoethanolamine (MEA), NH2CH2CH2OH to absorb the CO2 from the air.
The aqueous solution is then regenerated by passing it through a column of packed glass rings and by heating it to drive off the CO2 under pressure. As shown below.
H-O-CH2-CH2-NH-CO-OH  H-O-CH2-CH2–NH2 +O=C=O
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 23: ?
4. Activated Carbon Adsorption
A form of carbon that has been processed to make it highly porous so as to have a very large surface area available for adsorption or chemical reactions.
CO2 saturated air is passed over the activated carbon and the CO2 is adsorbed onto the surface.
Can be regenerated by blowing air with a low CO2 concentration through the bed.
Only useful to us if we have a waste stream of air from another process that can be used to clean it.
There is no way of gaining a pure CO2 stream, which may cause problems in later processes when converting the CO2 to O2. Therefore this technology is not applicable to the space station.
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 24: ?
5. Scrubbers
Soda Lime – used on submarines
Constant air circulation through a scrubber system filled with 75% calcium hydroxide. CO2 is removed via the following reaction.
CO2 + Ca(OH)2 → CaCO3 + H2O
Non regenerative, Ca(OH)2 must be resupplied.
Lithium Hydroxide – used in spacesuits
Used to remove CO2 from exhaled air by one of two reactions.
2 LiOH·H2O + CO2 → Li2CO3 + 3 H2O
2LiOH + CO2 → Li2CO3 + H2O
Second is lighter and produces less water.
Neither systems are regenerable and LiOH must be resupplied.
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 25: ?
Criteria & Constraints- CO2 Separation
Technology | Applicability | Reliability | Modularity | Resupply
CRDA |  |  |  | 
MEA Absorption |  |  |  | 
Activated Carbon |  | - | - | -
PSA |  |  |  | 
Sorbents |  |  |  | 
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 26: ?
Criteria & Constraints- CO2 Separation
Technology | Applicability | Reliability | Modularity | Resupply
CRDA |  |  |  | 
MEA Absorption |  |  |  | 
Activated Carbon |  | - | - | -
PSA |  |  |  | 
Sorbents |  |  |  | 
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 27: ?
CO2 Separation - Final 3
 | CDRA | MEA Absorption | PSA
Resupply (kg/18 months) | 0 | 0* | 0
No. of independent units | 2 | 2 | 2*
Feed streams | 1 | 1 | 1
Recovery rate (%) | - | 70-90 | 95*
Maintenance (years) | 3-5 | - | 3-5
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 28: ?
CO2 Separation - Final 3
 | CDRA | MEA Absorption | PSA
Resupply (kg/18 months) | 0 | 0* | 0
No. of independent units | 2 | 2 | 2*
Feed streams | 1 | 1 | 1
Recovery rate (%) | - | 70-90 | 95*
Maintenance (years) | 3-5 | - | 3-5
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 29: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis
Photocatalytic splitting
Thermolysis
Thermochemical cycles
Catalysis

## Slide 30: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis Cont…
Photocatalytic splitting
Advantages – simplicity (use catalyst suspended in water to electrolyse solution in the presence of sunlight)
Disadvantages – Critical system would depend on the availability of sufficient insolation
2. Thermolysis
Advantages - Can use methane as a fuel (if Sabatier is used)
Disadvantages – Extremely high temperatures (2000°C) required to split water which means high rate of component failure.

## Slide 31: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis Cont…
3. Thermochemical Cycles
Advantages – Relatively low temperature (530°C for Cu-Cl cycle).
Disadvantages – Requires several different reactors and chlorine gas may be produced which is a potential problem.
4. Catalysis (Milstein 3 stage process).
Advantages – Low temperature (100°C) and fairly simple system, can be scaled up.
Disadvantages – Relatively new technology, may require more research before it is a viable alternative to electrolysis.

## Slide 32: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis Cont…
Alternatives to Electrolysis Cont…
5. Bipolar Electrolysis
Advantages – Developed from monopolar electrolyzer. Low energy consumption and high efficiency make it suitable to scale up.
Disadvantages – Compact conformation of this system lead to difficulty of initial design.
6. Laser
Advantages – Similar to photocatalystic splitting, use laser instead of sunlight, simplicity structure, can be used on Mars.
Disadvantages – Sensitive plant, low reliability and difficult to repair by astronauts. High Energy consumption.

## Slide 33: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis Cont…
Alternatives to Electrolysis Cont…
7. PEM Electrolyzer
Advantages – no electrolyte required in this system, high efficiency and reliability
Disadvantages – The materials of the anode and cathode are very expensive and cannot be scaled up
8. Solid Oxide Electrolyzer
Advantages - High efficiency, exhaust heat can be recycled to save energy.
Disadvantages –High operating temperatures (Over 1000°C) lead to low system reliability. Strong limitation on cell material

## Slide 34: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Criteria & Constraints- Alternatives to Electrolysis
Technology | Applicability | Reliability | Modularity | Resupply
Photocatalytic |  | - | - | -
Thermolysis |  | - | - | -
Thermochemical Cycles |  | ? |  | 
Catalysis |  | ? |  | 
Laser |  | - | - | -
Bipolar Electrolysis |  |  |  | 
PEM Electrolyzer |  | - | - | -
Solid Oxide Electrolyzer |  | - | - | -

## Slide 35: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CO2 Treatment
RWGS
Sabatier
Bosch
Bosch-Boudouard

## Slide 36: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Criteria & Constraints- CO2 treatment
Technology | Applicability | Reliability | Modularity | Resupply
RWGS |  |  |  | 
Sabatier |  |  |  | 
Bosch |  |  |  | 
Bosch-Boudouard |  | n/a |  | 

## Slide 37: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Criteria & Constraints- CO2 treatment
Technology | Applicability | Reliability | Modularity | Resupply
RWGS |  |  |  | 
Sabatier |  |  |  | 
Bosch |  |  |  | 
Bosch-Boudouard |  | n/a |  | 

## Slide 38: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
 | Sabatier | RWGS
Resupply (kg/18 months) | 2343.5 | 1334.2
No. of independent units | 1 | 1
Feed streams | 2 | 2
Maintanence | Unknown | Unknown
CO2 treatment – Final Two

## Slide 39: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
 | Sabatier | RWGS
Resupply (kg/18 months) | 2343.5 | 1334.2
No. of independent units | 1 | 1
Feed streams | 2 | 2
Maintanence | Unknown | Unknown
CO2 treatment – Final Two

## Slide 40: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CO2 treatment
Feasibility studies for CO2 treatment methods indicate that the Sabatier reaction is the best choice for “stage 2”.
Possibility of improving the process in “stage 3” by recovering hydrogen from the methane, as opposed to venting it to Mars. This would create a closed loop for both H2 and O2, meaning neither would need to be resupplied.